## Slide 1
Wireless and Mobile Systems
for the IoT
Nirupam Roy
Tu-Th 12:30-1:45pm
IRB 2107
CMSC 715 : Fall 2023
Lecture: Midterm review

## Slide 2
November 9th, Thursday, 12:30 PM, Room: 2107
The exam questions will be spread over the topics taught so far (up to lecture 3.7).
Fundamental concepts/theories are important.
No programming.
An open (book, notes, phone, computer, Internet) exam.
Not open to discussions with humans. 
Exam logistics

## Slide 3
Lecture 1.1
Sensor fundamentals, Local/global coordinate systems, frequency and phase of a signal.
Lecture 1.2
Time & Frequency domain representation, Analog to Digital conversion, Sampling theorem,
Aliasing
Lecture 1.3
Complex representation of a signal, Positive and negative frequencies, Discrete Fourier Transform (DFT)
Lecture 1.4
Plot DFT spectrum, properties of DFT, Aliasing in different types of signals, Frequency bands, multiplication of frequency.
Midterm syllabus

## Slide 4
Lecture 2.1
-- (continued from lecture 1.4): Antialiasing filter, multiplication of frequencies, frequency bands, Sampling a band of frequencies.
-- Time-space propagation of signals (waves), reflection and echolocation, using waves for proximity sensing and ranging (distance finding)
Lecture 2.2
-- An example technique for estimating distance using sound wave (application: contact tracing), reference paper: “BeepBeep: A High-Accuracy Acoustic-Based System for Ranging”
-- Space-time equation of waves
Lecture 2.3
Phase difference of signal due to location difference, Superposition of waves, Sensing with multiple sensors, Spatial filtering/beamforming in 1-D space
Lecture 2.4
Spatial filtering/beamforming in 2-D space,
Directional sensing with the sensor array, uniform linear array (ULA)
Lecture 2.5
The direction of arrival estimation (Delay sum method, classical FFT method)
Lecture 2.6
RFIDraw paper discussion

## Slide 5
Lecture 3.1
Markov model, Hidden Markov Model
Lecture 3.2
Hidden Markov Model (continued from last lecture)
Lecture 3.3
Viterbi decoding
An example project on the application of Bayesian inference: “MoLe: Motion Leaks through Smartwatch Sensors”
Lecture 3.4 & Lecture 3.5
Continued discussion on Bayesian inference and the paper “MoLe: Motion Leaks through Smartwatch Sensors”
Lecture 3.6
Owlet paper discussion.

## Slide 6
Following papers were discussed in the class and will be included in the syllabus:
BeepBeep: A High-Accuracy Acoustic-Based System for Ranging: https://www.cs.purdue.edu/homes/chunyi/pubs/peng-tecs12.pdf
RF-IDraw: Virtual Touch Screen in the Air Using RF Signals
https://deepakv.web.illinois.edu/assets/papers/RF-IDraw_SIGCOMM_2014.pdf
3) I am a Smartwatch and I can Track my User’s Arm
https://sinrg.csl.illinois.edu/papers/ArmTrak_Mobisys.pdf
4) MoLe: Motion Leaks through Smartwatch Sensors: https://synrg.csl.illinois.edu/papers/mole.pdf
5) Owlet: enabling spatial information in ubiquitous acoustic devices
https://www.cs.umd.edu/~nirupam/images/2_publication/papers/Owlet_MobiSys21_nirupam.pdf

## Slide 7
Bayesian inference, Markov Model, HMM
Beam-steering
ULA
2. Short answer type (15 points)
Sampling, DFT/FFT, aliasing
Superposition of signal, Wavelength, Space-time equation
HMM and Viterbi
Concepts from the papers discussed in the class
3. Problem solving (35 points)
Sensor basics, Sampling theory, Aliasing, FFT spectrum, Echolocation,
Wave propagation, Space-time equation of wave, beamforming or spatial filtering, ULA
1. Multiple choice questions (10x2 = 20 points)
Question format (tentative)

## Slide 8
Sensor Basics (Lecture 1.1)

## Slide 9
A physical phenomenon
We want to measure
A structure or material
that reacts to the physical phenomenon
A circuit that converts the reaction to measurable electrical signal (e.g. voltage)
Interpretation of the signal, storing the data
SENSOR

## Slide 10
X
Y
Scalar and vector output
Global coordinate system

## Slide 11
X
Y
Local coordinate system
Coordinate system

## Slide 12
X
Y
Vx
Vy
Local coordinate system
Coordinate system
Output at time t
<Vx (t), Vy(t), Vz(t)>
for a 3-axis sensor
Z

## Slide 13
Coordinate system

## Slide 14
North
East
Global coordinate system
Coordinate system
Local coordinate system
X
Y
Z

## Slide 15
Time Domain and Frequency Domain
Time domain view
Frequency domain view

## Slide 16
Frequencies of an arbitrary signal

## Slide 17
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
The concept of the Fourier series

## Slide 18
Sampling, Aliasing, Complex representation of signal (Lecture 1.2)

## Slide 19
A physical phenomenon
We want to measure
A structure or material
That reacts to the physical phenomenon
A circuit that converts the reaction to measurable electrical signal (e.g. voltage)
Interpretation of the signal, storing the data
SENSOR
Digital
Analog
Analog

## Slide 20
Physical signal
(voice)
Time varying voltage
signal
Spectrogram plot
on computer
FFT
A collection of numbers
Analog
Digital
ADC
Analog-to-Digital Converter

## Slide 21
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
[ 0.34 0.22 0.09 0.21 0.30 0.08 0.09 ]
Sampling theorem
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00

## Slide 22
1-dimensional sampling
2-dimensional sampling
3-dimensional sampling

## Slide 23
Aliasing

## Slide 24
How to find a good sample rate?
Nyquist-Shannon sampling theorem:
In order to uniquely represent a signal F(t) by a set of samples, the sampling rate must be more than twice the highest frequency component present in F(t).
If sample rate is fs and maximum frequency we want to
record is fmax , then
fs > 2fmax

## Slide 25
Model for a signal (frequency, amplitude, and phase)

## Slide 26
Presenting real signal with the complex model
2
2j

## Slide 27
Time-frequency views of signal, DFT/FFT
(Lecture 1.3)

## Slide 28
Time Domain and Frequency Domain
Time domain view
Frequency domain view

## Slide 29
Frequencies of an arbitrary signal

## Slide 30
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
The concept of the Fourier series

## Slide 31
Discrete Fourier Transform
=
X =
x[0]
…
…
…
…
…
Z0
Z1
Zm
ZN-1
+
+
+
…
x[1]
x[2]
x[N-1]
…
Time domain samples
Frequency domain coefficients

## Slide 32
Discrete Fourier Transform
DFT matrix,
F
=
f0
f1
fm
fN-1
…
…

## Slide 33
Discrete Fourier Transform
DFT matrix,
F
=
f0
f1
fm
fN-1
…
…
Fourier coefficients,
Z
=
Z0
Z1
Zm
ZN-1
…
…
X =
x[0]
x[1]
x[2]
x[N-1]
…
Time series,

## Slide 34
Discrete Fourier Transform
X
=
F
Z
Z
=
F-1
X
Z
=
F
X
f0
f1
fm
fN-1
…
…
*
*
*
*
Z0
Z1
Zm
ZN-1
…
…
x[0]
x[1]
x[2]
x[N-1]
…
=
DFT
IDFT
H

## Slide 35
Properties of DFT
(Lecture 1.4 & continued to 2.1)

## Slide 36
Time resolution v/s Frequency resolution

## Slide 37
U
M
D
[
[
DFT
DFT
How can we increase the frequency resolution?
=
How can we increase the time resolution?
Time resolution v/s Frequency resolution

## Slide 38
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
The Curious Case of “Negative frequency”
Real signal’s magnitude spectrum is symmetric.
Why?
Magnitude
|zm|

## Slide 39
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
The Curious Case of “Negative frequency”
Complex signal’s magnitude spectrum may or may not be symmetric.
Why?
Magnitude
|zm|

## Slide 40
Aliasing: Different frequencies, same name!!
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
Magnitude/Phase of zm
Assume, Sample rate = 8 Hz
For a COMPLEX signal, what value will we see if the actual frequency is:
a) 3 Hz
b) -2 Hz
c) 6 Hz
d) -5 Hz
e) 4 Hz and -4Hz

## Slide 41
Aliasing: Different frequencies, same name!!
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
Magnitude/Phase of zm
Assume, Sample rate = 8 Hz
For a REAL signal, what value will we see if the actual frequency is:
a) 3 Hz
b) -2 Hz
c) 6 Hz
d) -5 Hz
e) 4 Hz and -4Hz

## Slide 42
Amplitude
4
Frequency (Hz)
0
6
8
2
Sampling frequency = 10Hz
Nyquist frequency = 5Hz
Calculating the aliased frequency value for real signals

## Slide 43
Amplitude
4
Frequency (Hz)
0
6
8
2
Sampling frequency = 10Hz
Amplitude
4
Frequency (Hz)
0
6
8
2
Nyquist frequency = 5Hz
Received
signal
Calculating the aliased frequency value for real signals

## Slide 44
Calculating the aliased frequency value for real signals
Amplitude
4
Frequency (Hz)
0
6
8
2
Sampling frequency = 10Hz
Amplitude
4
Frequency (Hz)
0
6
8
2
Nyquist frequency = 5Hz
Received
signal
fs = Sampling frequency
f = Target frequency
fa = Aliased(perceived) frequency
K = Non-negative integer
fa = min(abs(K*fs - f))

## Slide 45
10k
20k
30k
40k
50k
60k
70k
80k
90k
100k
Frequency spectrum
Amplitude
Nyquist frequency
Aliasing: A real life scenario
Notes: to amplify the signal power …
Now, this signal typically contains many more frequencies than the sampling system can handle …

## Slide 46
10k
20k
30k
40k
50k
60k
70k
80k
90k
100k
Frequency spectrum
Amplitude
Nyquist frequency
Aliasing: A real life scenario
Notes: to amplify the signal power …
Now, this signal typically contains many more frequencies than the sampling system can handle …

## Slide 47
Frequency spectrum
Nyquist frequency
10k
20k
30k
40k
50k
60k
70k
80k
90k
100k
Amplitude
We need a “Low-pass filter”
to remove unwanted high frequency signals
Aliasing: A real life scenario
Notes: to amplify the signal power …
Now, this signal typically contains many more frequencies than the sampling system can handle …

## Slide 48
10k
20k
30k
40k
50k
60k
70k
80k
90k
100k
ADC
Amplitude
Sensor
Frequency spectrum
Anti-aliasing
Filter
Anti-aliasing filter
Nyquist frequency
Notes: Hence, a low pass filter…

## Slide 49
Anti-aliasing
filter
10k
20k
30k
40k
50k
60k
70k
80k
90k
100k
Anti-aliasing
Filter
ADC
Amplitude
Sensor
Frequency spectrum
Anti-aliasing filter
Notes: removes the unwanted frequencies above 24 kHz …
And ultimately, this filtered signal is sampled by an ADC to generate digital sound samples

## Slide 50
A few more ideas…
1) Filtering frequencies
2) Multiplying frequency with frequency
1) Filtering frequencies
3) Sampling a band of frequencies

## Slide 51
0
What should be the sample rate?
Amplitude
4
Frequency (kHz)
0
6
8
2
Sample Rate for a Frequency band

## Slide 52
Sample Rate for a Frequency band
Amplitude
4
Frequency (kHz)
0
6
8
2
What should be the sample rate?
Amplitude
4
Frequency (kHz)
0
6
8
2
Frequency
down-conversion
Generally, bandwidth of the signal determines the sample rate.

## Slide 53
Waves propagation, echolocation
(Lecture 2.1)

## Slide 54
Sound
WiFi signal
Physical vibrations
Visible light
Ripples in water
Infrared
…
…
Mechanical Wave
Electromagnetic Wave

## Slide 55
Waves in time and space
Temporal variation of the wave’s amplitude

## Slide 56
Waves in time and space

## Slide 57
Waves in time and space

## Slide 58
Waves in time and space

## Slide 59
Waves in time and space

## Slide 60
echo
Absorption
+
Reflection
Reflection

## Slide 61
Sound travelled (2d) distance
d
t2
Time = t1
echo
Absorption
+
Reflection
Echolocation

## Slide 62
Sound travelled (2d) distance
d
t2
Time = t1
C.(t2-t1) = 2d
echo
Absorption
+
Reflection
Echolocation

## Slide 63
Distance between devices (Beep-Beep)
(Lecture 2.2)

## Slide 64
How to find the proximity between two smartphones?

## Slide 65
A simple acoustic ranging technique
BeepBeep – SenSys 2007

## Slide 66: Timeline
tA3
2nd Beep
tB3
tB2
1st Beep
tB1
tA0
tA1
ETOAA
ETOAB
P
Q
|ETOAA-ETOAB|
= (P+Q+P) – (Q)
= 2P
= 2 (time of flight)
Device A
Device B
P

## Slide 67
Time-space equation of waves
(Lecture 2.3)

## Slide 68
Equation of waves in time and space
(t, x)
= λ

## Slide 69
= λ
= /
Equation of waves in time and space

## Slide 70
Equation of waves in time and space
(t, x)
= λ

## Slide 71
Equation of waves in time and space
(t, x)
= λ

## Slide 72
Time and space
Cycles per sec = frequency = f Hz
Distance per second = speed = C meters/sec
Distance per cycle = wavelength = λ meters
C = f . λ
Speed of sound in air: 343 m/s
Speed of sound in water: 1493 m/s
Speed of sound in iron: 5130 m/s
Speed of electromagnetic waves: 3*108 m/s
(~ a million times faster than sound)

## Slide 73
Distance = d meter
Time and space

## Slide 74
Distance = d meter
d meter
Time and space

## Slide 75
d = X.sin()
Time and space
X meters

## Slide 76
Spatial filtering (controlling signal gain in space)

## Slide 77
Alexa!
Spatial filtering

## Slide 78
Spatial filtering

## Slide 79
Superimposition of signals
Spatial filtering (controlling signal gain in space)

## Slide 80
(in space)
Spatial filtering (controlling signal gain in space)
Superimposition of signals

## Slide 81
Superimposition of sinusoids

## Slide 82
Superimposition of sinusoids

## Slide 83
Superimposition of sinusoids

## Slide 84
Superimposition of sinusoids
=
=
Signal nullified
Signal nullified
Signal amplified
(perfect constructive interference)

## Slide 85
Array of sensors, ULA, beamforming
(Lecture 2.4)

## Slide 86
Beamforming in 2D space

## Slide 87
Beamforming in 2D space
Phase difference between these two paths

## Slide 88
Near vs Far Field
Assume far-field (planar wave model) when the receiver/transmitter are (2L2/ λ) distance apart.

## Slide 89
Beamforming in 2D space
Approximation for ‘far field’
()
Combined signal =
Along this line
=

## Slide 90
Beamforming in 2D space
+
Combined signal
=

## Slide 91
Beamforming in 2D space
Directional gain of an array

## Slide 92
Beamforming in 2D space

## Slide 93
Directionality of signals: Physical guiding

## Slide 94
Directionality of signals: Array of sensors

## Slide 95
Uniform Linear Array (ULA)

## Slide 96
Beamforming in 2D space
()
…
N elements
()
()
Interelement distance = d
Path difference with nth element:
()
Phase difference with nth element:
() 2Π/λ

## Slide 97
()
…
N elements
()
()
Path difference with nth element:
()
Phase difference with nth element:
() 2Π/λ
Beamforming in 2D space
Signal at 1st sensor:
Combined signal:

## Slide 98
Beamforming in 2D space
Angle
Gain
-90 -60 -30 0 30 60 90
Notes: http://www.waves.utoronto.ca/prof/svhum/ece422/notes/15-arrays2.pdf

## Slide 99
Beamforming in 2D space

## Slide 100
Angle of arrival detection (Lecture 2.5)

## Slide 101
Angle-of-Arrival (AoA)
or
Direction-of-Arrival (DoA)

## Slide 102
DoA Estimation: Beam-scanning
Scan the region with a steerable beam of the phased array.
DoA of the signal will show maximum received power.

## Slide 103
DoA Estimation: Delay-sum

## Slide 104
Discrete Fourier Transform for DoA
asin( )
2
Sample number
3
4
1
6
N-1
5
0
…

## Slide 105
Statistical inference (Lecture 3.1)

## Slide 106
A few basic probability rules
Likelihood of multiple events occurring simultaneously
Joint probability: P (A, B) = P (B, A)
Conditional probability: P (A|B) = P(A,B)/P(B)
Probability of an event, given another event has occurred
Marginal probability: P (B) =
Chain rule: P (A, B, C) = P(A|B,C) P(B,C) = P(A|B,C) P(B|C) P(C)

## Slide 107
Bayes rule
Posterior
Prior
Likelihood
=
Bayes rule: P (Ai|B) =

## Slide 108
Markov Model
Sunny
day
Rainy
day
Sunny
Sunny
Rainy
Sunny
Rainy
Rainy
P (sunny after sunny)
P (rainy after sunny)
P (sunny after rainy)
P (rainy after rainy)
t1 t2 t3 t4 t5 t6 (time)
Mth order Markov assumption: Current state depends on past M states

## Slide 109
Hidden Markov Model

## Slide 110
Hidden Markov Model
Sunny
day
Rainy
day
Sunny
Sunny
Rainy
Sunny
Rainy
Rainy
P (sunny after sunny)
P (rainy after sunny)
P (sunny after rainy)
P (rainy after rainy)
Temp.
Humidity
Wind
Temp.
Humidity
Wind
t1 t2 t3 t4 t5 t6 (time)

## Slide 111
1st order Markov assumption:
Transition probability depends on the current state only.
Output independence assumption:
Output/Emission probability depends on the current state only.
M1
S1
Emission
S2
S1
Transition
Hidden Markov Model: Definition

## Slide 112
Observation depends on the current state only
Future state depends on the current state only
Hidden Markov Model: Definition

## Slide 113
Problems solved by HMM
1) Likelihood:
  Determine the likelihood of an observation sequence.
2) Decoding:
  Given an observation sequence, determine the best sequence of hidden states.
3) Learning:
  Given an observation sequence and a sequence of states, learn the HMM parameters:
  i) Transition probabilities
  ii) Emission probabilities
[Viterbi algorithm]
[Forward-backward algorithm]
[Baum-Welch algorithm]

## Slide 114
HMM and Viterbi algorithm
(Lecture 3.2 & Lecture 3.3)

## Slide 115
Problems solved by HMM
1) Likelihood:
  Determine the likelihood of an observation sequence.
2) Decoding:
  Given an observation sequence, determine the best sequence of hidden states.
3) Learning:
  Given an observation sequence and a sequence of states, learn the HMM parameters:
  i) Transition probabilities
  ii) Emission probabilities
[Viterbi algorithm]
[Forward-backward algorithm]
[Baum-Welch algorithm]

## Slide 116
Near
Far
Observations:
Call
No
Call
States:
A simple gesture recognition example
Notes: http://www.davidsbatista.net/assets/documents/posts/2017-11-11-hmm_viterbi_mini_example.pdf

## Slide 117
Call
No
Call
A simple gesture recognition example
Near
Far
Near
Far
Start
End
St
0.7
0.7
0.3
0.2
0.7
0.2
0.1
0.1
1
0.7
0.3
0.4
0.6

## Slide 118
A simple gesture recognition example
 | Call | NoCall | End
Start | 0.7 | 0.3 | 0
Call | 0.2 | 0.7 | 0.1
NoCall | 0.7 | 0.2 | 0.1
 | St | Near | Far
Start | 1 | 0 | 0
Call | 0 | 0.7 | 0.3
NoCall | 0 | 0.4 | 0.6
State transition
probabilities
Emission
probabilities

## Slide 119
A simple gesture recognition example
Emission states are: Near, Far, Far
What is the hidden state sequence?

## Slide 120
Start
Call
No
Call
Call
No
Call
Call
No
Call
End
Near
A simple gesture recognition example
Far
Far
St
i = 1 2 3

## Slide 121
Hidden Markov Model: Definition

## Slide 122
A simple gesture recognition example
[Ref] http://www.davidsbatista.net/assets/documents/posts/2017-11-11-hmm_viterbi_mini_example.pdf
Recursion
Save two parameters per iteration, per state:

## Slide 123
A simple gesture recognition example
Call
No
Call
Call
Near
Far
i = 1 2

## Slide 124
Start
Call
No
Call
Call
No
Call
Call
No
Call
End
Near
A simple gesture recognition example
Far
Far
i = 1 2 3
St

## Slide 125
Start
Call
No
Call
Near
A simple gesture recognition example
i = 1
 | Call | NoCall | End
Start | 0.7 | 0.3 | 0
Call | 0.2 | 0.7 | 0.1
NoCall | 0.7 | 0.2 | 0.1
 | St | Near | Far
Start | 1 | 0 | 0
Call | 0 | 0.7 | 0.3
NoCall | 0 | 0.4 | 0.6
State transition probabilities
Emission probabilities
St

## Slide 126
A simple gesture recognition example
Start
Call
No
Call
Call
No
Call
Near
Far
i = 1 2

## Slide 127
Start
Call
No
Call
Call
No
Call
Call
No
Call
End
Near
A simple gesture recognition example
Far
Far
i = 1 2 3
0.343
0.14406
0.0043
0.04116

## Slide 128
Start
Call
No
Call
Call
No
Call
Call
No
Call
End
Near
A simple gesture recognition example
Far
Far
i = 1 2 3
The values of delta and psi are not correct on this slide. Please refer to the calculation shown at the following link.
http://www.cs.umd.edu/class/fall2020/cmsc818w/course_materials/slides/Viterbi_solution.pdf

## Slide 129
Start
Call
No
Call
Call
No
Call
Call
No
Call
End
Near
A simple gesture recognition example
Far
Far
i = 1 2 3
0.343
0.14406
0.0043
0.04116

## Slide 130
Start
Call
No
Call
Call
No
Call
Call
No
Call
End
Near
A simple gesture recognition example
Far
Far
i = 1 2 3
0.343
0.14406
0.0043
0.04116

## Slide 131
Start
Call
No
Call
Call
No
Call
Call
No
Call
End
Near
A simple gesture recognition example
Far
Far
i = 1 2 3
0.343
0.14406
0.0043
0.04116
Viterbi sequence: < Call, NoCall, Call >
P( <Call, NoCall, Call > | <Near, Far, Far>) = 0.0043
For complete step by step solution of this example visit:
http://www.cs.umd.edu/class/fall2022/cmsc715/course_materials/slides/Viterbi_solution.pdf

## Slide 132
Bayesian Inference (Lecture 3.4 & Lecture 3.5)

## Slide 133
A sample applications of statistical inference in IoT

## Slide 134: MoLe Motion Leaks through Smartwatch Sensors
He Wang
Ted Tsung-Te Lai
Romit Roy Choudhury
UIUC
MobiCom’15 Presentation
Continued from the last lecture

## Slide 135
MoLe Architecture
Bayesian
Inference
P(O|Wi)
Rank of Wordi
Attacker Point Cloud
Unlabeled Point Cloud
Observation ( O )
Word Wi
Keystroke
Detector
Time
a b c d
Attacker Training Data
User Data
Location
Dictionary
Point
Cloud
Fitting

## Slide 136
Bayesian Inference
Likelihood function
Wi: Candidate wordi in dictionary
O: Motion observation

## Slide 137
Bayesian Inference
Number of keystrokes
Location distribution
Time interval distribution
The probability of the observed motion given wordi
Number of keystrokes
Location distribution
Time interval distribution

## Slide 138
I am a Smartwatch and I can Track my User’s Arm
Sheng Shen, He Wang, Romit Roy Choudhury

## Slide 139
Understanding human arm motion
How is the arm moving?
What is the meaning of this motion?

## Slide 140
How is the arm moving?
What is the meaning of this motion?
Gesture Recognition
Posture Tracking

## Slide 141: Elbow Location Inferencing
t
Possible Elbow Locations
Elbow Acceleration
Location
Velocity
Acceleration
State 1

## Slide 142: RF-IDraw: Virtual Touch Screen in the Air
Deepak Vasisht
Jue Wang, Dina Katabi

## Slide 143: Ambiguity-Resolution Tradeoff
Ambiguity in position
Low resolution
High resolution
No ambiguity

## Slide 144: Localization
Are we done?

## Slide 145
Owlet: Enabling Spatial Information in Ubiquitous Acoustic Devices
http://icosmos.cs.umd.edu/project-owlet.html
Notes: Hi everyone, I am Nakul Garg, and (Yang says) and I am Yang Bai. Today we are going to present our paper called “Owlet: Enabling Spatial Information in Ubiquitous Acoustic Devices”. This is a joint work with our advisor Nirupam Roy. We are from the University of Maryland, College Park.

## Slide 146
Owlet: Sound localization with deep learning

## Slide 147
Acoustic micro-structures
Stencil
Mic
f
Sound direction = θ1
f
Sound DoA = θ2
f
Signature_θ1
Signature_θ2
f
Practical challenges for Owlet
Notes: Similarly, sound coming from another angle creates another unique signature. We collect these signatures from one-time calibration, and later use them to estimate the angle.

## Slide 148
System Design
Direction-specific impulse response
reference mic (outside the stencil)
environment impulse response
Notes: We have introduced a reference microphone placed outside the stencil.
When the same sound is received by the reference microphone, it will only be affected an environmental impulse response and Yout is equal to product of X and H environment prime.

## Slide 149
System Design
Dividing
One-time learning
Depends on external environment
Notes: But, the ratio of these impulse responses depend on the external environment.

## Slide 150
System Design
Reference microphone
Microphone inside stencil
Freq. spectrum
Phase spectrum
Predicted Angle
Synthetic dataset
Notes: We take advantage of the bounded distribution of this ratio and simulate multiple environments to create a synthetic dataset.
Then we train a neural network on the frequency and phase spectrums of this signal. Once trained, it can work in any arbitrary environment and estimate the angle in real time.