## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2023
Topic: Midterm-2 Review

## Slide 2
Midterm exam -2.
April 13th in-class exam.
Midterm-2 syllabus: Lecture 8 to 18
Exam format: Similar to exam-1

## Slide 3: CIDR: Classless address

## Slide 4
CIDR: Classless InterDomain Routing
  Network portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
200.23.16.0–200.23.17.255
IP addressing: CIDR
This X bit network part is often called Prefix or Network-prefix

## Slide 5
IP addressing: CIDR
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
forwarding table
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address

## Slide 6: CIDR: Super-netting/ Route aggregation

## Slide 7
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Forwarding tab.
223.1.0.0/16
223.1.0.0/16

## Slide 8
200.20.1.0/24
200.20.2.0/24
200.20.3.0/24

## Slide 9
200.20.1.0/24
200.20.2.0/24
200.20.3.0/24

## Slide 10
200.20.1.0/24
200.20.2.0/24
200.20.3.0/24
Route aggregation

## Slide 11
Route aggregation with CIDR

## Slide 12
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homing
Forwarding tab.
201.10.0.0/21
201.10.6.0/23

## Slide 13: CIDR Makes Packet Forwarding Harder
Forwarding table may have many matches
  E.g., entries for 201.10.0.0/21 and 201.10.6.0/23
  The IP address 201.10.6.17 would match both!
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2

## Slide 14: Longest Prefix Match Forwarding
Destination-based forwarding
  Packet has a destination address
  Router identifies longest-matching prefix
  Cute algorithmic problem: very fast lookups
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
201.10.6.17
destination
forwarding table
outgoing link

## Slide 16: Getting an IP address: DHCP Protocol

## Slide 17: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 18
Broadcast: is there a DHCP server out there?

## Slide 19
inet 10.104.216.101  00001010.01101000.11011000.01100101
netmask ff:ff:f0:00  11111111.11111111.11110000.00000000
broadcast 10.104.223.255 
00001010.01101000.11011111.11111111

## Slide 20
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 21: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 22: DHCP relay
Newly booted or attached host sends DHCPDISCOVER message to a special IP address (255.255.255.255)
DHCP relay agent unicasts the message to DHCP server and waits for the response

## Slide 23
Lecture 9

## Slide 25: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers

## Slide 26: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 28: Network address vs LAN address

## Slide 29
Destination
Source
Router
Two perspectives of addresses:
(1)Network-to-network & (2)machine-to-machine

## Slide 30
Source
Router
application
transport
network
link
physical
network
link
physical
Flat address for addressing machines at the link-layer
(MAC address)

## Slide 31: Address Resolution Protocol (ARP)

## Slide 32: MAC addresses and ARP
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD

## Slide 33: MAC addresses and ARP
each adapter on LAN has unique LAN addr. or MAC addr.
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)

## Slide 34: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 35: ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 36
Lecture 10

## Slide 37: Internet Control Message Protocol (ICMP)
Defines a collection of error messages that are sent back to the source host whenever a router or host is unable to process an IP datagram successfully
  Destination host unreachable due to link /node failure
  Reassembly process failed
  TTL had reached 0 (so datagrams don't cycle forever)
  IP header checksum failed
ICMP-Redirect
  From router to a source host
  With a better route information

## Slide 38
ICMP message types

## Slide 39
Ping example

## Slide 40
Traceroute : An unintuitive application using ICMP

## Slide 41
Traceroute : An unintuitive application

## Slide 43
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
Untrusted/Shared network

## Slide 44
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
New IP Header Source: Gateway-A Dest: Gateway-A
IP Header
Data
Decapsulation
New IP Header Source: Gateway-A Dest: Gateway-A
IP Header
Data
Untrusted/Shared network
Encapsulation

## Slide 45
Why do we need virtual networks or tunnels?
1. Security
2. Special capabilities between routers (e.g., multicast)
3. Supporting heterogeneity
Disadvantages:
1. Increases packet length
a) Wastage of bandwidth
b) More processing
c) Fragmentation
2. Increases management cost

## Slide 47: IPv6
1) Address and packet format
2) Unicast, Multicast, Anycast addressing
3) IPV4 and IPV6 coexistence

## Slide 48: IPv6: Address and packet format
Pic courtesy: https://techhub.hpe.com

## Slide 49: IPv6: Unicast, Multicast, Anycast addressing

## Slide 50: IPv6: Unicast, Multicast, Anycast addressing
IP: Anycast example

## Slide 51: IPv4 and IPv6 Co-existence

## Slide 52
Lecture 11

## Slide 53: Transport Protocols
Logical communication between processes
  Sender divides a message into segments
  Receiver reassembles segments into message
Transport services
  (De)multiplexing packets
  Detecting corrupted data
  Optionally: reliable delivery, flow control, …

## Slide 54: Two Basic Transport Features
Demultiplexing: port numbers
Error detection: checksums
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
OS
Client
IP
payload
detect corruption

## Slide 55
Connection-less mux/demux:
- User Datagram Protocol (UDP)
Connection-oriented mux/demux:
- Transmission Control Protocol (TCP)

## Slide 56: Connectionless demultiplexing
Create sockets with port numbers:
DatagramSocket mySocket1 = new DatagramSocket(99111);
DatagramSocket mySocket2 = new DatagramSocket(99222);
UDP socket identified by two-tuple:
(dest IP address, dest port number)
When host receives UDP segment:
  checks destination port number in segment
  directs UDP segment to socket with that port number
IP datagrams with different source IP addresses and/or source port numbers directed to same socket

## Slide 57: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
recv host uses all four values to direct segment to appropriate socket
Server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
Web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 59
End-to-end Protocols
(UDP, TCP)

## Slide 60: End-to-end Protocols
Common properties that a transport protocol can be expected to provide
  Guarantees message delivery
  Delivers messages in the same order they were sent
  Delivers at most one copy of each message
  Supports arbitrarily large messages
  Supports synchronization between the sender and the receiver
  Allows the receiver to apply flow control to the sender
  Supports multiple application processes (Mux/DeMux)

## Slide 61: UDP: User Datagram Protocol [RFC 768]
Bare minimum Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others

## Slide 62: UDP checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected.
Goal: detect “errors” (e.g., flipped bits) in transmitted segment
Is UDP service == IP service ??

## Slide 63: Advantages of UDP
Fine-grain control
  UDP sends as soon as the application writes
No connection set-up delay
  UDP sends without establishing a connection
No connection state
  No buffers, parameters, sequence #s, etc.
Small header overhead
  UDP header is only eight-bytes long

## Slide 64
Lec 12

## Slide 65
Transmission Control Protocol (TCP)

## Slide 66: TCP “Stream of Bytes” Service
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
Byte 80

## Slide 67: …Emulated Using TCP “Segments”
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
TCP Data
TCP Data
Byte 80
Segment sent when:
Segment full (Max Segment Size),
Not full, but times out, or
“Pushed” by application.

## Slide 68: Sequence Number
Host A
Host B
TCP Data
TCP Data
ISN (initial sequence number)
Sequence number =
ISN+ # of the 1st byte the segment
Byte 81

## Slide 69: Initial Sequence Number (ISN)
Sequence number for the very first byte
  E.g., Why not a de facto ISN of 0?
Practical issue: reuse of port numbers
  Port numbers must (eventually) get used again
  … and an old packet may still be in flight
  … and associated with the new connection
So, TCP must change the ISN over time
  Set from a 32-bit clock that ticks every 4 microsec
  … which wraps around once every 4.55 hours!

## Slide 70: Starting and Ending a Connection: TCP Handshakes (Three-Way Handshake)

## Slide 71: Establishing a TCP Connection
Three-way handshake to establish connection
  Host A sends a SYN (open) to the host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
SYN
SYN ACK
ACK
Data
A
B
Data
Each host tells its ISN to the other host.

## Slide 72
TCP Header

## Slide 75: Step 1: A’s Initial SYN Packet
A’s port
B’s port
A’s Initial Sequence Number
Acknowledgment
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
A tells B it wants to open a connection…

## Slide 78: Step 2: B’s SYN-ACK Packet
B’s port
A’s port
B’s Initial Sequence Number
A’s ISN plus 1
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
B tells A it accepts, and is ready to hear the next byte…
… upon receiving this packet, A can start sending data

## Slide 81: Step 3: A’s ACK of the SYN-ACK
A’s port
B’s port
B’s ISN plus 1
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
A tells B it is okay to start sending
Sequence number
… upon receiving this packet, B can start sending data

## Slide 82: What if the SYN Packet Gets Lost?
Suppose the SYN packet gets lost
  Packet is lost inside the network, or
  Server rejects the packet (e.g., listen queue is full)
Eventually, no SYN-ACK arrives
  Sender sets a timer and wait for the SYN-ACK
  … and retransmits the SYN if needed
How should the TCP sender set the timer?
  Sender has no idea how far away the receiver is
  Some TCPs use a default of 3 or 6 seconds

## Slide 83: Tearing Down the Connection
Closing (each end of) the connection
  Finish (FIN) to close and receive remaining bytes
  And other host sends a FIN ACK to acknowledge
  Reset (RST) to close and not receive remaining bytes
SYN
SYN ACK
ACK
Data
FIN
ACK
ACK
time
A
B
FIN
ACK

## Slide 85: TCP Acknowledgments
Host A
Host B
TCP Data
TCP Data
ISN (initial sequence number)
Sequence number = ISN+1st byte
ACK sequence number = next expected byte

## Slide 86: Automatic Repeat reQuest (ARQ)
ACK and timeouts
  Receiver sends ACK when it receives packet
  Sender waits for ACK and times out
Simplest ARQ protocol
  Stop and wait
  Send a packet, stop and wait until ACK arrives
Time
Packet
ACK
Timeout
Sender
Receiver

## Slide 87: Automatic Repeat reQuest (ARQ)
We will discuss two variations
  1. Stop and Wait
  2. Sliding window

## Slide 88
Lec 13

## Slide 89: Stop and Wait

## Slide 90
Time
Packet
ACK
Timeout
Sender
Receiver

## Slide 91: Reasons for Retransmission
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
ACK lost
DUPLICATE PACKET
Packet lost
Early timeout
DUPLICATE PACKETS
Notes: Application may get duplicates in the case of early timeouts

## Slide 92: How Long Should Sender Wait?
Sender sets a timeout to wait for an ACK
  Too short:
  >> wasted retransmissions
  Too long:
  >> excessive delays when packet lost
TCP sets timeout as a function of the RTT
  Expect ACK to arrive after a “round-trip time”
  … plus a fudge factor to account for queuing
But, how does the sender know the RTT?
  Running average of delay to receive an ACK

## Slide 93
Example RTT Estimation

## Slide 95: Reliable Delivery on a Lossy Channel With Bit Errors
TCP Flow control: Sliding Window Protocol

## Slide 96
Revisiting “delay X bandwidth”

## Slide 97
Revisiting “delay X bandwidth”

## Slide 98
Revisiting “delay X bandwidth”
Consider two-way delay
or round-trip delay

## Slide 99: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Network bandwidth = R bits-per-sec
Packet size = L bits

## Slide 100: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Network bandwidth = R bits-per-sec
Packet size = L bits
1kB packet per 30.008 msec
~33KB/sec throughput over a 1GBPS link!!

## Slide 101: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Network bandwidth = R bits-per-sec
Packet size = L bits
1kB packet per 30.008 msec
~33KB/sec throughput over a 1GBPS link!!
Network protocol limits the full utilization of physical resources.
Transport-layer vs Link-layer capacity gap

## Slide 102: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
Increase utilization
by a factor of 3!

## Slide 103
Sliding Window Protocol

## Slide 104
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Packet 1 is delivered. Slide the window.
Window = # pkt in flight
Sent
Sent

## Slide 105
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Packet 1 is delivered. Slide the window.
Window = # pkt in flight
Sent
Sent
Sent

## Slide 106
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Should we advance the window in the following scenario?
Window = # pkt in flight
Sent
Sent
Sent
ACK
Note that the window size is not changed!

## Slide 107
Sliding Window Protocol
(dealing packet loss)

## Slide 108
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent
(1) ARQ strategy 1: Retransmit all un-ACKed packets
Re-tx
Re-tx
Re-tx

## Slide 109
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent
(2) ARQ strategy 2: Retransmit only the lost packet
Re-tx
(2) Selective retransmit (Sender side)

## Slide 111
TCP Cumulative ACK strategy (receiver side)
(A more specific example)
X
Seq. # | 234118
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234268
ACK flag | N/A
ACK # | N/A
Data Len | 120 bytes
Seq. # | 234388
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234218
ACK flag | N/A
ACK # | N/A
Data Len | 50 bytes

## Slide 112
TCP Cumulative ACK strategy (receiver side)
(A more specific example)
X
Seq. # | 234118
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234268
ACK flag | N/A
ACK # | N/A
Data Len | 120 bytes
Seq. # | 234388
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234218
ACK flag | N/A
ACK # | N/A
Data Len | 50 bytes
Timeout

## Slide 113
TCP Cumulative ACK strategy (receiver side)
(A more specific example)
X
Seq. # | 234118
Data Len | 100 bytes
Seq. # | 234268
Data Len | 120 bytes
Seq. # | 234388
Data Len | 100 bytes
Seq. # | 234218
Data Len | 50 bytes
ACKs
ACK flag | 1
ACK # | 234218
ACK flag | 1
ACK # | 234218
ACK flag | 1
ACK # | 234218
ACK flag | 1
ACK # | 234488

## Slide 114: Flow Control: TCP Sliding Window (Recap)
Motivation: Maximum utilization of the resources without overwhelming the receiver.

## Slide 115
How to send the Advertised_Window size

## Slide 116
Calculate Advertised_Window (Receiver side)
Receiving process
TCP
Next byte expected
Last byte read
Last byte received
AdvertisedWindow = MaxRcvBuffer –
((NextByteExpected-1) – LastByteRead)
AdvertisedWindow = MaxRcvBuffer – (bytes used)

## Slide 117
Sender buffer
Receiver buffer
AdvertisedWindow = MaxRcvBuffer –
((NextByteExpected-1) – LastByteRead)
EffectiveWindow (calculated at the sender side)
= AdvertisedWindow - (LastByteSent – LastByteACKed)
What if the AdvertisedWindow is zero?
>> Periodically send 1byte packets to break the deadlock. (uses the persist timer)

## Slide 119: A few points of discussions on TCP flow control
Silly window syndrome
Nagle’s algorithm (self-clocking)
Karn-Partridge algorithm

## Slide 120
Lec 15

## Slide 121
TCP: Abstraction of Reliable Bytes Stream

## Slide 122
Congestion Collapse
Notes: Picture: https://ocw.mit.edu/courses/electrical-engineering-and-computer-science/6-829-computer-networks-fall-2002/lecture-notes/L8e2ecc.pdf

## Slide 123: How TCP detects packet losses
(2) Timeout
  Packet# n is lost and detected via a timeout
(1) Duplicate ACKs
  Packet# n is lost, but packets n+1, n+2, etc. are received and ACKs are sent.

## Slide 124: TCP Congestion Control

## Slide 125
ACK works as the indicator and the window controls the flow.
Congestion_window: Calculated by the sender

## Slide 126: Two Kinds of Loss in TCP
(2) Timeout (Repeat slow start – slow start restart)
  Packet n is lost and detected via a timeout
  Blasting entire CWND would cause another burst
  Better to start over with a low CWND
(1) Triple duplicate ACK (Fast retransmit)
  Packet n is lost, but packets n+1, n+2, etc. arrive
  Then, sender quickly resends packet n
  Do a multiplicative decrease and keep going

## Slide 127: Repeating Slow Start After Timeout (slow-start restart)
t
Window
Slow-start restart: Go back to CWND of 1, but take advantage of knowing the previous value of CWND.
Slow start until reaching half of previous cwnd.
timeout
Packet loss (3-dup ack, fast retransmit)

## Slide 128
Lec 16

## Slide 129
Implementation details
Update Time: Per RTT vs Per ACK
Double CWND per round-trip time
D
A
D
D
A
A
D
D
A
A
D
A
Src
Dest
D
A
1
2
4
8
Implemented as CWND = CWND + 1 (per ACK)

## Slide 130
Implementation details
Update Time: Per RTT vs Per ACK
Linear increase of CWND per round-trip time
D
A
D
D
A
A
D
D
A
A
D
A
Src
Dest
D
A
1
2
3
4
Implemented as CWND = CWND + 1/CWND (per ACK)

## Slide 131: TCP congestion control: CWND graph
CWND = 1
First packet loss (3-dup acks)
CWND = CWND/2
Congestion avoidance CWND = CWND + (1/CWND)
Packet loss
(3-dup acks)
CWND = CWND/2
Time out(no acks)
SSTHRES = CWND/2
Slow Start restart
Slow Start end
Congestion
avoidance
CWND =
CWND +
(1/CWND)
Slow start
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 132: TCP Reno: details of Fast Recovery
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 133: TCP Reno: details of Fast Recovery
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 134
TCP Congestion Control

## Slide 135: TCP versions
TCP is not perfectly homogenous (200+)
4.2 BSD first widely available release of TCP/IP (1983)
4.3 BSD (1986)
4.3 BSD Tahoe (1988)
4.3 BSD Reno (1990)
Vegas (1994)
Windows 95
SunOS 4.1.3,4.1.4
4.4 BSD (1993)
HP/UX
Solaris 2.3,2.4
Digital OSF
Windows NT
Linux 1.0
IRIX
.....
NewReno (1999)
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 136: 2. Router-assisted Congestion Control
Copyright, 1996 © Dale Carnegie & Associates, In

## Slide 137: Bursty Loss From Drop-Tail Queuing
TCP depends on packet loss
  Packet loss is indication of congestion
  TCP additive increase drives network into loss
Drop-tail leads to bursty loss
  Congested link: many packets encounter full queue
  Synchronization: many connections lose packets at once

## Slide 138: Random Early Detection (RED)
Router notices that queue is getting full
  … and randomly drops packets to signal congestion
Packet drop probability
  Drop probability increases as queue length increases
  Else, set drop probability f(avg queue length)
Average Queue Length
Drop
Probability
0 1

## Slide 139: Feedback: From Loss to Notification
Early dropping of packets
  Good: gives early feedback
  Bad: has to drop the packet to give the feedback
Explicit Congestion Notification (ECN)
  Router marks the packet with an ECN bit
  Sending host interprets as a sign of congestion
  Requires participation of hosts and the routers

## Slide 140: Link Scheduling
FIFO
  One queue, trivial scheduler
Strict priority
  One queue per priority level, simple scheduler
Weighted fair scheduling
  One queue per class, and more complex scheduler

## Slide 141
Lec 17

## Slide 142
TCP Congestion Control

## Slide 143
TCP Selective ACK (SACK): RFC 2018
https://www.rfc-editor.org/rfc/rfc2018

## Slide 144
Slides courtesy: https://cseweb.ucsd.edu/classes/wi01/cse222/lectures/attack-18.pdf