## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2025
Topic: DHCP, NAT, ARP, ICMP
(Textbook chapter 3)
March 10th, 2025

## Slide 2
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use
<Request> Broadcast: OK. I’ll take that IP address! Can I ?
<Ack>
Broadcast: OK. You’ve got that IP address!
Discussion Point 1: The transaction ID (xid). RFC 2131
Discussion Point 2: Broadcast address. (Limited/Directed broadcast)
Notes: RFC 2131, Page [39]: The DHCP client broadcasts DHCPDISCOVER, DHCPREQUEST and DHCPINFORM messages, unless the client knows the address of a DHCP server. The client unicasts DHCPRELEASE messages to the server.
DHCP is not intended for use in configuring routers.

## Slide 3
Broadcast traffic is sent to all stations on a LAN.
There are two types of IPv4 broadcast addresses:
Limited broadcast: The limited broadcast address is
255.255.255.255. It is “limited” because it is never forwarded across a router.
(b) Directed broadcast: The directed (also called net-directed) broadcast address of the 192.0.2.0/24 network is 192.0.2.255 (the host portion of the address is all “1”s in binary, or 255). It is called “directed” broadcast, because traffic to these addresses may be sent from remote networks (it may be “directed”).
Broadcast addresses: Limited and Directed broadcast

## Slide 4: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 5: Dynamic Host Configuration Protocol (DHCP)
DHCP server is responsible for providing configuration information to hosts
DHCP server maintains a pool of available addresses
There is at least one DHCP server for an administrative domain (a server or a relay agent per subnet)

## Slide 6: DHCP relay
Newly booted or attached host sends DHCPDISCOVER message to a special IP address (255.255.255.255)
DHCP relay agent unicasts the message to DHCP server and waits for the response

## Slide 7
Check your IP addresses
ifconfig (linux/mac) / ipconfig (windows)

## Slide 8
Check your IP addresses
(ifconfig/ipconfig)

## Slide 9: Private Address Space & NAT

## Slide 11: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers

## Slide 12
What is a Port number?
Computer 1
Computer 2
IP addr-1
IP addr-2
Process - 1
Process - 2
Process - n
Process - 1
Process - 2
Process - n
1001
263
2039
211
716
456
16-bit integers
called ‘port numbers’
Notes: An internet port number can be as large as 65,535. This is because port numbers are 16-bit integers, meaning they can represent values from 0 to 65,535.
Key points about port numbers:
Range:
0 - 65,535
Well-known ports:
Ports from 0 to 1023 are considered "well-known" and are assigned to commonly used services like HTTP (port 80).
Registered ports:
Ports from 1024 to 49151 are registered ports that can be used by applications to identify specific services.
Dynamic ports:
Ports from 49152 to 65,535 are considered "dynamic" or "ephemeral" and are used for temporary connections by applications.

## Slide 13: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 14: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 15: NAT: network address translation
implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 16: NAT: network address translation
implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 17: NAT: network address translation
16-bit port-number field:
  Over 60,000 simultaneous connections with a single LAN-side address!
NAT challenges:
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  NAT traversal: what if client wants to connect to server behind NAT?

## Slide 18: Network-specific address (IP address) vs LAN-specific address (HW address)

## Slide 19
Destination
Source
Router
Two perspectives of addresses:
(1)Network-to-network & (2)machine-to-machine

## Slide 20
Source
Router
application
transport
network
link
physical

## Slide 21
Source
Router
network
link
physical
application
transport
network
link
physical

## Slide 22
Router
Hierarchical address for addressing networks
(IP address)
network
link
physical

## Slide 23
Source
Router
application
transport
network
link
physical
network
link
physical

## Slide 24
Source
Router
application
transport
network
link
physical
network
link
physical
Flat address for addressing machines at the link-layer
(MAC address)

## Slide 25: Address Resolution Protocol (ARP)

## Slide 26: MAC addresses and ARP
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)

## Slide 27: MAC addresses and ARP
each adapter on LAN has unique LAN addr. or MAC addr.
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 28: MAC addresses (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address not portable
  address depends on IP subnet to which node is attached

## Slide 29: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 30: ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 31: Address Translation Protocol (ARP)
Map IP addresses into physical addresses
  destination host
  next hop router
Techniques
  encode physical address in host part of IP address
  table-based
ARP (Address Resolution Protocol)
  table of IP to physical address bindings
  broadcast request if IP address not in table
  target machine responds with its physical address
  table entries are discarded if not refreshed
  Query message include the physical address of the sending host. Why?

## Slide 32: ARP Packet Format
  HardwareType: type of physical network (e.g., Ethernet)
  ProtocolType: type of higher layer protocol (e.g., IP)
  HLEN & PLEN: length of physical and protocol addresses
  Operation: request or response
  Source/Target Physical/Protocol addresses

## Slide 33: Internet Control Message Protocol (ICMP)

## Slide 34: Internet Control Message Protocol (ICMP)
Defines a collection of error messages that are sent back to the source host.
E.g., ICMP messages are sent whenever a router or host is unable to process an IP datagram successfully
  Destination host unreachable due to link /node failure
  Reassembly process failed
  TTL had reached 0 (so datagrams don't cycle forever)
  IP header checksum failed
ICMP-Redirect
  From router to a source host
  With a better route information

## Slide 35
ICMP message types

## Slide 36
Ping example

## Slide 37
Traceroute : An unintuitive application using ICMP

## Slide 38
Traceroute example

## Slide 39
Traceroute : An unintuitive application

## Slide 40: Virtual Networks and Tunnels

## Slide 41
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Untrusted/Shared network

## Slide 42
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
Untrusted/Shared network

## Slide 43
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
New IP Header Source: Gateway-A Dest: Gateway-B
IP Header
Data
Encapsulation
Untrusted/Shared network

## Slide 44
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
New IP Header Source: Gateway-A Dest: Gateway-B
IP Header
Data
Decapsulation
New IP Header Source: Gateway-A Dest: Gateway-B
IP Header
Data
Untrusted/Shared network

## Slide 45
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
IP Header
Data
Untrusted/Shared network

## Slide 46
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
New IP Header Source: Gateway-A Dest: Gateway-A
IP Header
Data
New IP Header Source: Gateway-A Dest: Gateway-A
IP Header
Data
Encryption/Decryption
Untrusted/Shared network

## Slide 47
Trusted network (Site A)
Trusted network (Site B)
Untrusted/Shared network
Gateway A
Gateway B
Virtual Tunnel
Virtual Private Network
(VPN)

## Slide 48
Why do we need virtual networks or tunnels?
1. Security
2. Special capabilities between routers (e.g., multicast)
3. Supporting heterogeneity

## Slide 49
Why do we need virtual networks or tunnels?
1. Security
2. Special capabilities between routers (e.g., multicast)
3. Supporting heterogeneity
Disadvantages:
1. Increases packet length
a) Wastage of bandwidth
b) More processing
c) Fragmentation
2. Increases management cost

## Slide 50: IPv6
1) Address and packet format
2) Unicast, Multicast, Anycast addressing
3) IPV4 and IPV6 coexistence

## Slide 51: IPv6: Address and packet format
Pic courtesy: https://techhub.hpe.com

## Slide 52: IPv6: Address and packet format
Pic courtesy: https://techhub.hpe.com
Q 1. Why is there no header checksum?
Q 2. Why is there no fragmenting related option?
Q 3. Is 128-bit IP address big enough?
Notes: IPv6 provides for a maximum of 3.4×10^38 (340 trillion trillion trillion) unique IP addresses, or about 47 octillion unique addresses for every person on the planet.
For comparison: One light-year is about 6 trillion miles (9 trillion km)

## Slide 53: Unicast, Multicast, Anycast, Broadcast

## Slide 54: Unicast, Multicast, Anycast, Broadcast
IPv4
IPv4
IPv4

## Slide 55: Unicast, Multicast, Anycast, Broadcast
IPv4
IPv4
IPv4
IPv6
IPv6
IPv6

## Slide 56: Unicast, Multicast, Anycast, Broadcast
IP: Anycast example

## Slide 57: IPv4 and IPv6 Co-existence

## Slide 58: IPv4 and IPv6 Co-existence

## Slide 59
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2023
Topic:
Transport Layer Protocols (UDP, TCP)
(Textbook chapter 5)
March 5th, 2024

## Slide 61
Transport layer: From the lens of two perspectives
(1) Abstraction of clients. (machines/networks/processes)
(2) Abstraction of services.

## Slide 62
(1) Abstraction of clients

## Slide 63
Network 1
Network 2
Network 3
128.2.0.0/16
16.20.0.0/20
200.30.0.0/16
Network layer abstraction

## Slide 64
Network 1
Network 2
Network 3
128.2.0.0/16
16.20.0.0/20
200.30.0.0/16
Network layer abstraction

## Slide 65
Network 1
Network 2
Network 3
128.2.0.0/16
16.20.0.0/20
200.30.0.0/16
Network layer abstraction
Network layer services

## Slide 66
Transport layer abstraction

## Slide 67
Transport layer abstraction
Transport layer services

## Slide 69
Connection between processes

## Slide 70
Implementation of networking algorithms

## Slide 71: Transport Protocols
Logical communication between processes
  Sender divides a message into segments
  Receiver reassembles segments into message
Transport services
  (De)multiplexing packets
  Detecting corrupted data
  Optionally: reliable delivery, flow control, …

## Slide 72: Two Basic Transport Features
Demultiplexing: port numbers
Error detection: checksums
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
OS
Client
IP
payload
detect corruption

## Slide 73: Multiplexing/demultiplexing
application
transport
network
link
physical
P1
application
transport
network
link
physical
application
transport
network
link
physical
P2
P3
P4
P1
host 1
host 2
host 3
= process
= socket
delivering received segments
to correct socket
Demultiplexing at rcv host:
Data headers helps flows
from multiple sockets to use
common the network channel,
Info in header later helps
Demultiplexing.
Multiplexing at send host:

## Slide 74: How demultiplexing works
1) host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries 1 transport-layer segment
  each segment has source, destination port number
2) host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format

## Slide 75
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 76
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 77
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 78
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 79
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2