## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2025
Topic: TCP Flow-control and Congestion-control
(Textbook chapter 5 & 6)
March 26th, 2025

## Slide 2: Automatic Repeat reQuest (ARQ)
We will discuss two variations
  1. Stop and Wait
  2. Sliding window

## Slide 3: Reliable Delivery on a Lossy Channel With Bit Errors
Stop-and-Wait Protocol

## Slide 4
Time
Packet
ACK
Timeout
Sender
Receiver

## Slide 5
A few design decisions
  1. Unique packet identifiers: Why and how
  2. Duplicate packets: Why and how to eliminate
  3. Timeout: picking the ideal value

## Slide 6
A few design decisions
  1. Unique packet identifiers: Why and how
  2. Duplicate packets: Why and how to eliminate
  3. Timeout: picking the ideal value

## Slide 7
PC: https://en.wikipedia.org/wiki/Transmission_Control_Protocol
Receive, ACKed, sent to APP
Receive, ACKed, not sent to APP
Receive, not ACKed
Unused buffer

## Slide 8
REF: RFC 1323
Wrap around is possible

## Slide 9
REF: RFC 1323
If A and B are sequence numbers,
A < B if 0 < (B - A) < 2**31,
computed in signed 32-bit arithmetic
Wrap around-aware sequence number comparison
(modulo arithmatic)
PAWS: Protect Against Wrapped Sequence Numbers
(RFC 1323) – Use sequence number and timestamps.
Maximum segment lifetime (MSL, ~2 minutes) should be shorter than wrap-around-time, i.e., 2**31 / B > MSL (secs)

## Slide 10
A few design decisions
  1. Unique packet identifiers: Why and how
  2. Duplicate packets: Why and how to eliminate
  3. Timeout: picking the ideal value

## Slide 11
A few design decisions
  2. Duplicate packets: Why and how to eliminate
  - Receiver maintain the last in-sequence byte number in a variable, say rcv_seqnum
  - If the Receiver receives a packet with seq number less than or equal to rcv_seqnum

## Slide 12
A few design decisions
  2. Duplicate packets: Why and how to eliminate
  - Receiver maintain the last in-sequence byte number in a variable, say rcv_seqnum
  - If the Receiver receives a packet with seq number less than or equal to rcv_seqnum
  >>It sends an ACK for that packet, and discards the packet
  - If the Receiver receives a packet with seq number (rcv_seqnum+1):

## Slide 13
A few design decisions
  2. Duplicate packets: Why and how to eliminate
  - Receiver maintain the last in-sequence byte number in a variable, say rcv_seqnum
  - If the Receiver receives a packet with seq number less than or equal to rcv_seqnum
  >>It sends an ACK for that packet, and discards the packet
  - If the Receiver receives a packet with seq number (rcv_seqnum+1):
  >> It sends an ACK for that packet, and includes the packet to the application buffer

## Slide 14
A few design decisions
  2. Duplicate packets: Why and how to eliminate
  - Receiver maintain the last in-sequence byte number in a variable, say rcv_seqnum
  - If the Receiver receives a packet with seq number less than or equal to rcv_seqnum
  >>It sends an ACK for that packet, and discards the packet
  - If the Receiver receives a packet with seq number (rcv_seqnum+1):
  >> It sends an ACK for that packet, and includes the packet to the application buffer
  - What if the receiver gets a packet with seq number greater than (rcv_seqnum+1) ?

## Slide 15
A few design decisions
  3. Timeout: picking the ideal value
  - What if the timeout is too small?
  - What if the timeout is too large?
  - Round-Trip time (RTT)

## Slide 16
A few design decisions
  1. Unique packet identifiers: Why and how
  2. Duplicate packets: Why and how to eliminate
  3. Timeout: picking the ideal value

## Slide 17: Reasons for Retransmission
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
ACK lost
DUPLICATE PACKET
Packet lost
Early timeout
DUPLICATE PACKETS
Notes: Application may get duplicates in the case of early timeouts

## Slide 18: How Long Should Sender Wait?
Sender sets a timeout to wait for an ACK
  Too short:
  >> wasted retransmissions
  Too long:
  >> excessive delays when packet lost

## Slide 19: How Long Should Sender Wait?
Sender sets a timeout to wait for an ACK
  Too short:
  >> wasted retransmissions
  Too long:
  >> excessive delays when packet lost
TCP sets timeout as a function of the RTT
  Expect ACK to arrive after a “round-trip time”
  … plus a fudge factor to account for queuing
But, how does the sender know the RTT?

## Slide 20: How Long Should Sender Wait?
Sender sets a timeout to wait for an ACK
  Too short:
  >> wasted retransmissions
  Too long:
  >> excessive delays when packet lost
TCP sets timeout as a function of the RTT
  Expect ACK to arrive after a “round-trip time”
  … plus a fudge factor to account for queuing
But, how does the sender know the RTT?
  Running average of delay to receive an ACK

## Slide 21
TCP timestamp

## Slide 22
TCP timestamp
Sender’s current time

## Slide 23
TCP Timestamp Option (10 bytes)
Sender’s current time
Copied timestamp from the packet
being acknowledged.
(valid only when the packet contains an ACK.
i.e., the ACK bit is set in TCP header).

## Slide 24
Example RTT Estimation

## Slide 25: Reliable Delivery on a Lossy Channel With Bit Errors
TCP Flow control: Sliding Window Protocol

## Slide 26: Motivation for Sliding Window
Stop-and-wait is inefficient
  Only one TCP segment is “in flight” at a time
  Especially bad for high “delay-bandwidth product”
delay
bandwidth

## Slide 27
Revisiting “delay X bandwidth”

## Slide 28
Revisiting “delay X bandwidth”

## Slide 29
Revisiting “delay X bandwidth”

## Slide 30
Revisiting “delay X bandwidth”
Consider two-way delay
or round-trip delay

## Slide 31
Time
Packet
ACK
Round-trip delay
Sender
Receiver
Revisiting “delay X bandwidth”

## Slide 32: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Network bandwidth = R bits-per-sec
Packet size = L bits

## Slide 33: Performance – an implementation of stop-and-wait
Stop-and-wait works, but performance stinks
ex: 1 Gbps link, 15 ms prop. delay, 8kbit (8000 bit) packet:
  U sender: utilization – fraction of time sender busy sending
  1KB pkt every 30 msec -> 33kB/sec thruput over 1 Gbps link
  network protocol limits use of physical resources!

## Slide 34: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Network bandwidth = R bits-per-sec
Packet size = L bits
1kB packet per 30.008 msec

## Slide 35: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Network bandwidth = R bits-per-sec
Packet size = L bits
1kB packet per 30.008 msec
~33KB/sec throughput over a 1GBPS link!!

## Slide 36: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Network bandwidth = R bits-per-sec
Packet size = L bits
1kB packet per 30.008 msec
~33KB/sec throughput over a 1GBPS link!!
Network protocol limits the full utilization of physical resources.
Transport-layer vs Link-layer capacity gap

## Slide 37: A problem in rdt3.0

## Slide 38: Pipelined protocols
Pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
Two generic forms of pipelined protocols (or sliding window protocol) depending on the retransmission strategy: go-Back-N, selective repeat

## Slide 39: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
Increase utilization
by a factor of 3!

## Slide 40: Some Pipelining Protocols
Go-back-N: overview
sender: up to N unACKed pkts in pipeline
receiver: only sends cumulative ACKs
  doesn’t ACK pkt if there’s a gap
sender: has timer for oldest unACKed pkt
  if timer expires: retransmit all unACKed packets
Selective Repeat: overview
sender: up to N unACKed packets in pipeline
receiver: ACKs individual pkts
sender: maintains timer for each unACKed pkt
  if timer expires: retransmit only unACKed packet

## Slide 41: Go-Back-N
Sender:
k-bit seq # in pkt header
“window” of up to N, consecutive unACKed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  may receive duplicate ACKs (see receiver)
timer for each in-flight pkt
timeout(n): retransmit pkt n and all higher seq # pkts in window

## Slide 42
Time
Round-trip delay
Sender
Receiver
Revisiting “delay X bandwidth”

## Slide 43
Time
Packet
ACK
Timeout
Sender
Receiver
Sliding Window
Stop-and-wait

## Slide 44
Sliding Window: Lost Packet/ACK

## Slide 45
Sliding Window Protocol

## Slide 46
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent

## Slide 47
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent
ACK

## Slide 48
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Packet 1 is delivered

## Slide 49
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Packet 1 is delivered. Slide the window.
Window = # pkt in flight
Sent
Sent

## Slide 50
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Packet 1 is delivered. Slide the window.
Window = # pkt in flight
Sent
Sent
Sent

## Slide 51
Time
Sender
Receiver
Sliding Window: A series of packets to be sent reliably

## Slide 52
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Packet 1 is delivered. Slide the window.
Window = # pkt in flight
Sent
Sent
Sent

## Slide 53
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Should we advance the window in the following scenario?
Window = # pkt in flight
Sent
Sent
Sent
ACK

## Slide 54
Time
Sender
Receiver
Sliding Window: A series of packets to be sent reliably

## Slide 55
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Should we advance the window in the following scenario?
Window = # pkt in flight
Sent
Sent
Sent
ACK

## Slide 56
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Should we advance the window in the following scenario?
Window = # pkt in flight
Sent
Sent
Sent
ACK
Note that the window size is not changed!

## Slide 57
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent
Can you make sliding window behave like
stop-and-wait?

## Slide 58
Sliding Window Protocol
(dealing packet loss)

## Slide 59
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent

## Slide 60
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent
(1) ARQ strategy 1: Retransmit all un-ACKed packets
Re-tx
Re-tx
Re-tx

## Slide 61
Time
Timeout
Sender
Receiver
Sliding Window: A series of packets to be sent reliably
X
1
2
3
1
2
3
(1) Go-back-N (Sender side)

## Slide 62
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent
(2) ARQ strategy 2: Retransmit only the lost packet
Re-tx
(2) Selective retransmit (Sender side)

## Slide 63
Time
Timeout
Sender
Receiver
Sliding Window: A series of packets to be sent reliably
X
1
2
3
4
2
5
(2) Selective retransmit

## Slide 64
Sliding Window: Lost Packet/ACK
Timeout

## Slide 65
TCP Cumulative ACK strategy (receiver side)
Cumulative ACK:
ACK the largest in-sequence packet received.
What will be ACK sequence if the receive sequence
is: 5, 7, 8, 6 ?

## Slide 66
TCP Cumulative ACK strategy (receiver side)
Cumulative ACK:
ACK the largest in-sequence packet received.
What will be ACK sequence if the receive sequence
is: 5, 7, 8, 6 ?
ACK: 6, 6, 6, 9

## Slide 67
TCP Cumulative ACK strategy (receiver side)
(A more precise example)
X
Sender
Receiver

## Slide 68
TCP Cumulative ACK strategy (receiver side)
(A more specific example)
X
Seq. # | 234118
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234268
ACK flag | N/A
ACK # | N/A
Data Len | 120 bytes
Seq. # | 234388
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234218
ACK flag | N/A
ACK # | N/A
Data Len | 50 bytes
234118
234218
234268
234388
Sender
Receiver

## Slide 69
TCP Cumulative ACK strategy (receiver side)
(A more specific example)
X
Seq. # | 234118
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234268
ACK flag | N/A
ACK # | N/A
Data Len | 120 bytes
Seq. # | 234388
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234218
ACK flag | N/A
ACK # | N/A
Data Len | 50 bytes
Timeout
234118
234218
234268
234388
Sender
Receiver

## Slide 70
TCP Cumulative ACK strategy (receiver side)
(A more specific example)
X
Seq. # | 234118
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234268
ACK flag | N/A
ACK # | N/A
Data Len | 120 bytes
Seq. # | 234388
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234218
ACK flag | N/A
ACK # | N/A
Data Len | 50 bytes
234118
234218
234268
234388
234218
Sender
Receiver

## Slide 71
TCP Cumulative ACK strategy (receiver side)
(A more specific example)
X
Seq. # | 234118
Data Len | 100 bytes
Seq. # | 234268
Data Len | 120 bytes
Seq. # | 234388
Data Len | 100 bytes
Seq. # | 234218
Data Len | 50 bytes
234118
234218
234268
234388
234218
Sender
Receiver

## Slide 72
TCP Cumulative ACK strategy (receiver side)
(A more specific example)
X
Seq. # | 234118
Data Len | 100 bytes
Seq. # | 234268
Data Len | 120 bytes
Seq. # | 234388
Data Len | 100 bytes
Seq. # | 234218
Data Len | 50 bytes
ACKs
ACK flag | 1
ACK # | 
ACK flag | 1
ACK # | 
ACK flag | 1
ACK # | 
ACK flag | 1
ACK # | 
234118
234218
234268
234388
234218
Sender
Receiver

## Slide 73
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)

## Slide 74
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)
234118
100 bytes

## Slide 75
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)
234118
100 bytes
234218

## Slide 76
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)
234118
100 bytes
234218
234268
120 bytes

## Slide 77
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)
234118
100 bytes
234218
234268
120 bytes
234388
100 bytes

## Slide 78
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)
234118
100 bytes
234268
120 bytes
234388
100 bytes
234218
50 bytes

## Slide 79
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)
234118
100 bytes
234488
234268
120 bytes
234388
100 bytes
234218
50 bytes

## Slide 80
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
TCP Cumulative ACK strategy (receiver side)

## Slide 81
TCP Cumulative ACK strategy (receiver side)
(A more specific example)
X
Seq. # | 234118
Data Len | 100 bytes
Seq. # | 234268
Data Len | 120 bytes
Seq. # | 234388
Data Len | 100 bytes
Seq. # | 234218
Data Len | 50 bytes
ACKs
ACK flag | 1
ACK # | 234218
ACK flag | 1
ACK # | 234218
ACK flag | 1
ACK # | 234218
ACK flag | 1
ACK # | 234488
234118
234218
234268
234388
234218
Sender
Receiver

## Slide 82: Flow Control: TCP Sliding Window
Motivation: Maximum utilization of the resources without overwhelming the receiver.

## Slide 83
Sliding Window
Receiver should have enough space to buffer/save the received data !!

## Slide 84: Sliding Window: Implementation
Allow a larger amount of data “in flight” for better channel utilization, but should not exceed receiver’s capacity.
Sending process
Receiving process
Last byte ACKed
Last byte sent
TCP
TCP
Next byte expected
Last byte written
Last byte read
Last byte received
Window

## Slide 85: Sliding Window: Implementation
Allow a larger amount of data “in flight”
  Allow sender to get ahead of the receiver
  … though not too far ahead
Sending process
Receiving process
Last byte ACKed
Last byte sent
TCP
TCP
Next byte expected
Last byte written
Last byte read
Last byte received
Window

## Slide 86: Receiver Buffering: Flow control
Receive window size
  Amount that can be sent without acknowledgment
  Receiver must be able to store this amount of data
Receiver tells the sender the window
  Tells the sender the amount of free space left (i.e. sends an Advertised_Window size to the sender)

## Slide 87
How to send the Advertised_Window size

## Slide 88
Calculate Advertised_Window (Receiver side)
Receiving process
TCP
Next byte expected
Last byte read
Last byte received
AdvertisedWindow = MaxRcvBuffer –
((NextByteExpected-1) – LastByteRead)
AdvertisedWindow = MaxRcvBuffer – (bytes used)

## Slide 89
Sender buffer
Receiver buffer

## Slide 90
Sender buffer
Receiver buffer
AdvertisedWindow = MaxRcvBuffer –
((NextByteExpected-1) – LastByteRead)
EffectiveWindow (calculated at the sender side)
= AdvertisedWindow - (LastByteSent – LastByteACKed)
What if the AdvertisedWindow is zero?
>> Periodically send 1byte packets to break the deadlock. (uses the persist timer)

## Slide 91
(1) Adv_window > MSS
What if…
(2) Adv_window < MSS
Considering Maximum Segment Size (MSS)

## Slide 92
Sliding Window Protocol

## Slide 93
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent

## Slide 94
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent
ACK

## Slide 95
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Packet 1 is delivered

## Slide 96
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Packet 1 is delivered. Slide the window.
Window = # pkt in flight
Sent
Sent

## Slide 97
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Packet 1 is delivered. Slide the window.
Window = # pkt in flight
Sent
Sent
Sent

## Slide 98
Time
Sender
Receiver
Sliding Window: A series of packets to be sent reliably