## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2025
Topic: TCP Congestion-control and Link Layer
(Textbook chapters 6 & 2)
April 14th, 2025

## Slide 2
Slides courtesy: https://cseweb.ucsd.edu/classes/wi01/cse222/lectures/attack-18.pdf
Paper link: https://dl.acm.org/doi/10.1145/505696.505704

## Slide 10
Today’s TCP versions

## Slide 11
Today’s TCP versions
Mac OS-X
OS-X Mountain Lion (2012)  TCP New Reno
OS-X Mavericks (2023) to Sonoma (2023)  TCP CUBIC
Linux kernel
2.6.13 (2005)  TCP BIC (default)
2.6.19 (2006) to 6.7+ (2024)  TCP CUBIC (default)
Windows
Windows 8 (2013)  Compound TCP (CTCP)
Windows 10.1709 (2017) TCP CUBIC
Windows 11 (2021) TCP CUBIC

## Slide 12
BIC/CUBIC slides are adopted from: Injong Rhee, Lisong Xu, Ahmed El-Hassany, Qian HE, Bob Kinicki
TCP BIC: Issues with Reno
Notes: Slides adopted from: Injong Rhee, Lisong Xu, Ahmed El-Hassany

## Slide 13: Response Function of TCP
Response function of TCP is the average throughput of a TCP connection in terms of the packet loss probability, the packet size, and the round-trip time.
  R : Average Throughput
  MSS: Packet Size
  RTT: Round-Trip Time
  P : Packet Loss Probability
Response Function of TCP is :
J. Padhye, V. Firoio, D. Towsley, J. Kurose, "Modeling TCP Throughput: a Simple Model and its Empirical Validation", Proceedings of SIGCOMM 98
Notes: Usually, we study the performance of TCP using its response function, which is defined as the average throughput of TCP in terms of packet loss probability.
Here is the response function of TCP. In this function, MSS is the packet size, RTT is the round trip time, and p is the packet loss probability. From this function, we can see that the throughput of TCP depends on the packet size, the round-trip time, and the packet loss probability. In order to increase the throughput of TCP, we can either increase the packet size, or decrease the round trip time, or decrease the packet loss probability. Usually for a TCP connection, the packet size and round-trip time are fixed. Therefore, the throughput of a TCP connection mainly depends on the packet loss probability.

## Slide 14
x ms
y1 ms
y2 ms
z1 ms
z2 ms
y1 + x + z1 >> y2 + x + z2
TCP BIC: Issues with Reno – RTT unfairness

## Slide 15: Why BIC (Response Function of TCP)
10Gbps requires a packet loss rate of 10-10, or correspondingly a link bit error rate of at most 10-14, which is an unrealistic (or at least hard) requirement for current networks
Using Log-Log scale, Assuming 1250-Byte packet size, and 100ms RTT
Notes: In this figure, we show how the throughput changes as we vary the packet loss probability. Note that the figure is shown in log-log scale. We can see that as the packet loss probability decreases, the TCP throughput increases. Assume the packet size is 1000 Bytes, and the RTT is 100ms, then TCP achieves the 10Gbps throughput when the packet loss probability is around 10-10.which corresponds to a link BER of 10-14. which is an unrealistic requirement for current networks. That is, in the current networks, it is impossible for TCP to achieve 10Gbps throughput.

## Slide 16: A Search Problem
A Search Problem
  BIC consider the increase part of congestion avoidance as a search problem, in which a connection looks for the available bandwidth by comparing its current throughput with the available bandwidth, and adjusting cwnd accordingly.
How does standard TCP find the available bandwidth?
Linear search
  while (no packet loss){
  cwnd++;
  }
Q: How to compare R with A?
  R = current throughput
  = cwnd/RTT
  A = available bandwidth
A: Check for packet losses
  No packet loss: R <= A
  Packet losses : R > A

## Slide 17: Linear Search
Available Bandwidth

## Slide 18
TCP slowly increases its congestion window (cwnd) for every RTT.
TCP reduces cwnd by half at a lost event.
TCP BIC: Issues with Reno

## Slide 19
“Binary Increase Congestion Control (BIC) for Fast Long-Distance Networks”, Lisong Xu, Khaled Harfoush, and Injong Rhee, IEEE INFOCOM 2004
TCP BIC

## Slide 20
BIC - Binary search
  while (Wmin <= Wmax){
  inc = (Wmin+Wmax)/2 - cwnd;
  if (inc > Smax)
  inc = Smax;
  else if (inc < Smin)
  inc = Smin;
  cwnd = cwnd + inc;
  if (no packet losses)
  Wmin = cwnd;
  else
  break;
  }
Wmax: Max Window
Wmin: Min Window
Smax: Max Increment
Smin: Min Increment
TCP BIC: The algorithm

## Slide 21
If cwnd < low_window, normal TCP:
  ACK received
    cwnd = cwnd + 1
  Enter recovery
    cwnd = cwnd * 0.5
Else, BIC
TCP BIC: The algorithm

## Slide 22
BIC Algorithm
ACK received
  If cwnd < Wmax
    cwnd += (Wmax – cwnd) / 2
  Else
    cwnd += cwnd - Wmax
Recovery
  If cwnd < Wmax
    Wmax = cwnd * (1 – ß / 2)
  Else
    Wmax = cwnd
  cwnd *= 1 - ß
Smin <= cwnd
&&
cwnd <=Smax

## Slide 23
BIC with no lost
Chart: Time (RTT)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Linear Search | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Binary Search with Smax and Smin | 0 | 64 | 128 | 192 | 224 | 240 | 248 | 252 | 254 | 255 | 256
Smax
Smin

## Slide 24: Binary Search with Smax and Smin
Smin
Smax
Wmax
Wmin
Available Bandwidth

## Slide 25: Setting Smax
Response Function of BIC on high-speed networks
Bandwidth scalability of BIC depends only on Smax
RTT Fairness of BIC on high-speed networks is the same as that of AIMD
Bandwidth scalability

## Slide 26: Setting Smin
Response Function of BIC on low-speed networks
TCP-friendliness of BIC depends only on Smin
TCP friendliness

## Slide 27: In Summary BIC function
BIC overall performs very well in evaluation of advanced TCP stacks on fast long-distance production.
BIC (also HSTCP & STCP) growth function can be still aggressive for TCP especially under short RTTs or low speed networks.

## Slide 28
Make window size growth function independent from RTT.
Use the elapsed real-time since the last loss event.
Goals
  TCP friendly
  RTT fair
  Co-existing flows with different RTTs are treated fairly
  Efficient use of available bandwidth
In Summary BIC function

## Slide 29
Window control of BIC is so complex!
BIC’s growth function can still be too aggressive for TCP, especially under short RTT or low speed networks.
BIC still has room for improving TCP-friendliness and RTT-fairness!
29
TCP CUBIC: Why CUBIC?

## Slide 30: The CUBIC function
where C is a scaling factor, t is the elapsed time from the last window reduction, and β is a constant multiplication decrease factor
accelerate
accelerate
slow down

## Slide 31
ACK received
  C is a scaling factor
  t is the elapsed time from the last window reduction
  Wmax is the window size just before the last window reduction
  K is updated at the time of last lost event
Recovery
  Update K with:
  Update Wmax with:
  β is a constant multiplication decrease factor
TCP CUBIC: The algorithm
Notes: The CUBIC function (simplified):
cwnd(t)=C⋅(t−K)3+Wmaxcwnd(t)=C⋅(t−K)3+Wmax​Where:
t: Time since last congestion event
K: Time at which the function reaches Wma
C: Scaling constant (aggressiveness)
Wmax​: Last maximum congestion window
As t gets close to K, (t−K)3 approaches zero, and the function flattens near WmaxWmax​.

## Slide 32
ACK received
  C is a scaling factor
  t is the elapsed time from the last window reduction
  Wmax is the window size just before the last window reduction
  K is updated at the time of last lost event
Recovery
  Update K with:
  Update Wmax with:
  β is a constant multiplication decrease factor
cwnd cannot be less than
as to keep the growth rate the same as standard TCP in short RTT networks.
TCP CUBIC: The algorithm

## Slide 33
CUBIC window curves with competing flows (NS simulation in a network with 500Mbps and 100ms RTT), C = 0.4, β = 0.8.

## Slide 34
TCP ex Machina: Remy
Link to the paper: https://web.mit.edu/remy/TCPexMachina.pdf

## Slide 35
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2024
Topic: Link layer
(Textbook chapter 2)

## Slide 36
Protocol Layers
Notes: Picture Courtesy : https://microchipdeveloper.com/tcpip:tcp-ip-five-layer-model

## Slide 37: Link = Medium + Adapters

## Slide 38: What is a Link?
Communication Medium
Network Adapter

## Slide 39
Ripple: Communicating through Physical Vibrations
NSDI 2015
Vibration as medium

## Slide 41
Motion sensor
(accelerometer)
Vibration motor
Notes: Now, what could be the “RECEIVER” for such vibrations?
Observe that almost all mobile devices today have a motion sensor called … ACCELEROMETERS

## Slide 42
Motion sensor
(accelerometer)
Vibration motor
Notes: Thus, if the vibrating transmitter comes in CONTACT with the accelerometer … by literally TOUCHING the accelerometer … then the accelerometer can SENSE the vibrations and DECODE the data bits from it.
We have built such vibratory transmitters inside smartwatches and finger rings.
When the human finger touches the accelerometer … the vibration flows the the finger bone … and the data is transferred.
Of course, the human does not feel anything at all …

## Slide 43
Light as medium: LiFi

## Slide 44: Adaptors Communicating
Sending side
  Encapsulates packet in a frame
  Adds error checking bits, flow control, etc.
Receiving side
  Looks for errors, flow control, etc.
  Extracts datagram and passes to receiving node
sending
node
frame
receiving
node
packet
frame
adapter
adapter
link layer protocol
packet

## Slide 47: Link Layer Addresses (Recap) (Discussed earlier in the context of ARP)

## Slide 48: MAC addresses and ARP
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)

## Slide 49: ARP protocol
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 50: As an Aside: Promiscuous Mode
Normal adapter: receives frames sent to
  The local MAC address
  Broadcast address FF-FF-FF-FF-FF-FF
Promiscuous mode
  Receive everything, independent of destination MAC
Useful for packet sniffing
  Network monitoring
  E.g., wireshark, tcpdump

## Slide 51: Why Not Just Use IP Addresses?
Links can support any network protocol
  Not just for IP (e.g., IPX, Appletalk, X.25, …)
  Different addresses on different kinds of links
An adapter may move to a new location
  So, cannot simply assign a static IP address
  Instead, must reconfigure the adapter’s IP address
Must identify the adapter during bootstrap
  Need to talk to the adapter to assign it an IP address

## Slide 53: Collisions
Single shared broadcast channel
  Avoid having multiple nodes speaking at once
  Otherwise, collisions lead to garbled data
71-65-F7-2B-08-53
1A-2F-BB-76-09-AD
0C-C4-11-6F-E3-98

## Slide 54: Multi-Access Protocol
Divide the channel into pieces
  In time
  In frequency

## Slide 55: Multi-Access Protocol
Time Division Multiple Access
Frequency Division Multiple Access
Code Division Multiple Access

## Slide 56: Multi-Access Protocol
Divide the channel into pieces
  In time
  In frequency

## Slide 57: Multi-Access Protocol
Divide the channel into pieces
  In time
  In frequency
Take turns
  Pass a token for the right to transmit

## Slide 58: Multi-Access Protocol
Divide the channel into pieces
  In time
  In frequency
Take turns
  Pass a token for the right to transmit
Defer action
  Let collisions happen
  … and detect and recover from them
Carrier Sense Multiple Access

## Slide 59: Like Human Conversation…
Carrier sense
  Listen before speaking
  …and don’t interrupt!
Collision detection
  Detect simultaneous talking
  … and shut up!
Random access
  Wait for a random period of time
  … before trying to talk again!

## Slide 60: Carrier Sense Multiple Access (CSMA)

## Slide 61: Carrier Sense Multiple Access (CSMA)
Listen for other senders
  Then transmit your data
Collisions can still occur
  Propagation delay
  Wasted transmission

## Slide 62
CSMA: The time-space graph of collision

## Slide 63
CSMA: The time-space graph of collision

## Slide 64: CSMA: The time-space graph of collision

## Slide 65: CSMA: The time-space graph of collision
The time-space region of collision

## Slide 66: Comparing the Three Approaches
Divide the channel into pieces
  In time
  In frequency
Take turns
  Pass a token for the right to transmit
Defer action
  Let collisions happen
  … and detect and recover from them
Carrier Sense Multiple Access

## Slide 67: Comparing the Three Approaches
Channel partitioning
  Efficient and fair at high load
  Inefficient at low load
“Taking turns”
  Eliminates empty slots without collisions
  Vulnerable to failures (e.g. lost token)
Random access
  Efficient at low load
  Collision overhead at high load

## Slide 68
Automatic Repeat request
Flow control
Not implemented in wired LAN (e.g. Ethernet)

## Slide 69: Ethernet

## Slide 70: Ethernet
Dominant wired LAN technology
First widely used LAN technology
Kept up with speed race: 10 Mbps – 40 Gbps
Metcalfe’s
Ethernet
sketch

## Slide 72: Ethernet Uses CSMA/CD
Carrier Sense: wait for link to be idle
  Channel idle: start transmitting
  Channel busy: wait until idle
  A strategy is p-persistent if, after waiting for the line to clear, the sender sends with probability p≤1.
Collision Detection: listen while transmitting
  No collision: transmission is complete
  Collision: abort transmission, and send jam signal
Random Access: exponential back-off
  After collision, wait random time before trying again
  After mth collision, choose K randomly from {0, …, 2m-1}
  … and wait for K*512 bit times before trying again

## Slide 73: CSMA/CD Collision Detection
Detect collision
  Abort transmission
  Jam the link
Wait random time
  Transmit again
Hard in wireless
  Must receive data while transmitting

## Slide 74: CSMA/CD Collision Detection
Without collision detection
With collision detection and abort

## Slide 76
Collision does not happen like this. :-D

## Slide 77
Collision happens when both packet overlaps at the receiver.

## Slide 78
Preparing for the worst-case scenario of collision
Collision happens when both packet overlaps at the receiver.

## Slide 79
Thank you

## Slide 80
Preparing for the worst-case scenario of collision

## Slide 81
Preparing for the worst-case scenario of collision

## Slide 82
Preparing for the worst-case scenario of collision

## Slide 83
Preparing for the worst-case scenario of collision
The packet should be at least for 2d seconds long so that the sender can get the notification of the collision (through the jamming signal)

## Slide 84
Preparing for the worst-case scenario of collision
The packet should be at least for 2d seconds long so that the sender can get the notification of the collision (through the jamming signal)
Transmission time >= 2*propagation time

## Slide 85
Preparing for the worst-case scenario of collision
Formula for minimum packet size (P) or maximum length (L)

## Slide 86
Two questions
1. Why does the receiver send jamming signal after
detecting collision?
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.

## Slide 87
Two questions
Host A
Host B
Host C
1. Why does the receiver send jamming signal after
detecting collision?

## Slide 88
Two questions
Collision
Host C detects
collision
Host A
Host B
Host C
1. Why does the receiver send jamming signal after
detecting collision?

## Slide 89
Two questions
Collision
Attenuation makes
the signal weak. This may lead to missed detection.
Host A
Host B
Host C
1. Why does the receiver send jamming signal after
detecting collision?

## Slide 90
Two questions
Collision
Host A
Host B
Host C
Host B sends jamming signal to ensure collision
detection.
1. Why does the receiver send jamming signal after
detecting collision?

## Slide 91
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.

## Slide 92
Preparing for the worst-case scenario of collision

## Slide 93
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B

## Slide 94
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B
Collision

## Slide 95
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B
Collision

## Slide 96
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B
Collision
This situation is
not possible under our
assumptions.

## Slide 97
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B
Pkt: A
Valid scenario.

## Slide 98
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B
Pkt: A
Valid scenario.

## Slide 99
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B
Pkt: A
Not a valid scenario:
Host B won’t start transmission
as the channel is busy.

## Slide 100
Preparing for the worst-case scenario of collision

## Slide 102
Preparing for the worst-case scenario of collision
Repeater
(3 us delay)
Repeater
(3 us delay)

## Slide 103: Ethernet Frame Structure
Sending adapter encapsulates packet in frame
Preamble: synchronization
  Seven bytes with pattern 10101010, followed by one byte with pattern 10101011
  Used to synchronize receiver, sender clock rates

## Slide 104: Ethernet Frame Structure
Addresses: source and destination MAC addresses
  Adaptor passes frame to network-level protocol
    If destination is local MAC address or broadcast address
  Otherwise, adapter discards frame
Type: indicates the higher layer protocol
  Usually IP
  But also Novell IPX, AppleTalk, …
CRC: cyclic redundancy check
  Checked at receiver
  If error is detected, the frame is simply dropped

## Slide 105: Unreliable, Connectionless Service
Connectionless
  No handshaking between send and receive adapter
Unreliable
  Receiving adapter doesn’t send ACKs or NACKs
  Packets passed to network layer can have gaps
  Gaps can be filled by transport protocol (e.g., TCP)
  Otherwise, the application will see the gaps

## Slide 106: Star topology and collision-free Ethernet
Star topology
Bus topology

## Slide 107: Star topology and collision-free Ethernet
Star topology with hub and switch

## Slide 108: Repeaters, Hubs, Bridges and Switches

## Slide 111: Physical Layer: Repeaters
Distance limitation in local-area networks
  Electrical signal becomes weaker as it travels
  Imposes a limit on the length of a LAN
Repeaters join LANs together
  Analog electronic device
  Continuously monitors electrical signals
  Transmits an amplified copy

## Slide 112: Physical Layer: Hubs
Joins multiple input lines electrically
  Designed to hold multiple line cards
  Do not necessarily amplify the signal
Very similar to repeaters
  Also operates at the physical layer
hub
hub
hub
hub

## Slide 113
Physical Layer: Hubs

## Slide 114: Limitations of Repeaters and Hubs
One large shared link
  Each bit is sent everywhere
  So, aggregate throughput is limited
Cannot support multiple LAN technologies
  Does not buffer or interpret frames
  Can’t interconnect between different rates/formats
Limitations on maximum nodes and distances
  Shared medium imposes length limits
  E.g., cannot go beyond 2500 meters on Ethernet

## Slide 115: Link Layer: Bridges
Connects two or more LANs at the link layer
  Extracts destination address from the frame
  Looks up the destination in a table
  Forwards the frame to the appropriate segment
Each segment can carry its own traffic
host
host
host
host
host
host
host
host
host
host
host
host
Bridge

## Slide 116: Link Layer: Switches
Typically connects individual computers
  A switch is essentially the same as a bridge
  … though typically used to connect hosts
Supports concurrent communication
  Host A can talk to C, while B talks to D
switch
A
B
C
D

## Slide 117: Bridges/Switches: Traffic Isolation
Switch filters packets
  Frame only forwarded to the necessary segments
  Segments can support separate transmissions
hub
hub
hub
switch/bridge
segment
segment
segment

## Slide 118: Advantages Over Hubs/Repeaters
Only forwards frames as needed
  Avoid unnecessary load on segments
Wider geographic span
  Separate segments allow longer distances
Improves privacy
  Hosts can “snoop” traffic traversing their segment
  … but not all the rest of the traffic
Can join segments using different technologies

## Slide 119
Switch table
Traffic Isolation: Example

## Slide 120: Self Learning: Building the Table
When a frame arrives
  Inspect the source MAC address
  Associate the address with the incoming interface
  Store the mapping in the switch table
  Use a timer to eventually forget the mapping
A
B
C
D
Switch learns how to reach A.

## Slide 121: Self Learning: Handling Misses
When frame arrives with unfamiliar destination
  Forward the frame out all of the interfaces
  … except for the one where the frame arrived
  Hopefully, this case won’t happen very often!
A
B
C
D
When in doubt, shout!

## Slide 122
Exercise problems related to
learning-bridges/switches

## Slide 123
Switch vs Router

## Slide 124: Summary: Multiple Layers
Different devices switch different things
  Network layer: packets (routers)
  Link layer: frames (bridges and switches)
  Physical layer: electrical signals (repeaters and hubs)
Application
Transport
Router
Bridge, switch
Repeater, hub
Frame header
Packet header
TCP header
User
data